## Slide 1: FNAL beam test results update -- tracking for ref. detectors
A. Zhang, V. Bhopatkar, M. Phipps,
J. Twigger, M. Hohlmann
HEP Group A, Florida Tech
02/10/2014

## Slide 2: Tracking method - iteration
Alignment (shift)
Start from cluster position distributions. The distributions in both X and Y from 120GeV proton data can be fitted by Gaussian function. The mean values (times a factor of 20%) are taken as next shift parameters. The distributions in X for mixed beam can’t be fitted, but the mean (average) values also work.
Position dist. For REF2 in X
Proton data
Position dist. For REF2 in Y
Proton data
beam | REF2X | REF2Y | REF3X | REF3Y | UVA3X | UVA3Y | REF1X | REF1Y
32GeV | 3.6876 | 1.852 | -1.77 | -2.43 | -8.41 | 15.76 | -17.53 | -0.87
120GeV | 10.72 | 1.018 | 6.289 | -3.296 | -1.418 | 14.95 | -10.46 | -1.443
Unit mm

## Slide 3: Tracking method – a problem
For mixed beam data, when only shifting/aligning the detectors, the residual distributions give out two peaks.
The double-peak could be cleared by selecting specified events for tracking. Eg., set a 2mm range cut in X for the first ref. detector when selecting events.
3

## Slide 4: Tracking method - rotation
Rotation of detectors.
In REF2 system
In REF3 system
sin(α) = (x’y – xy’)/(x^2 + y^2)
Consider only rotation in XY plane (around Z).
Assume REF2 (the first ref. detector) is not rotated.
If detectors are fully aligned, the two coordinate systems have same origin in XY plane.
So the rotation angle α could be calculated. In the formula, (x,y) are from REF2, (x’,y’) from REF3
Angles from 120GeV proton data.
Once the angles are known, the positions in REF3 can be corrected.
Angle dist. between REF3 and REF2
REF3 | UVA3 | REF1
9.5mrad | -4.7mrad | -24.7mrad
4
4

## Slide 5: Tracking method – shift & rotate
Finally, we combined both shift and rotation in the tracking, it was working!
The initial shift parameters for proton and mixed beam data must be respective; but the initial rotation parameters must use those from proton data! (Use the angles calculated from mixed beam data could not disappear the double-peak)
The only explanation could be that the mixed data could not be used to calculate rotations angles because of wider beam size .
Mixed beam
proton beam

## Slide 6: Optimization of the rotation angles
The rotation angle for a single ref. detector can be optimized:
fixing all other parameters: all shift parameters and the other two rotation angles.
(2) Varying the tested angle in a small range near the calculated value.
(3) For each angle, fit all the tracks, and take the mean value of the χ2.
(4) We found that χ2 curve vs the angle is parabolic, the vertex point gives the minimum angle.
χ2 of tracks in XZ plane vs REF3 angle
χ2 of tracks in YZ plane vs REF3 angle
Avg. angle 4.85mrad

## Slide 7
Rotation angle for UVA3-REF2: -17.35mrad (avg.)
Rotation angle for REF1-REF2: -48.5mrad (avg.)

## Slide 8
Rotation angle for REF3-REF2: -3.9mrad (avg.)
Again, fixed angle of UVA3-REF2=-17.35mrad, REF1-REF2=-48.5mrad, get the angle of REF3-REF2=3.9mrad (avg.). ~1mrad smaller than the previous one.

## Slide 9: Residual distributions @ angles: REF3: 4mrad; UVA3: -17.35mrad; REF1: -48.5mrad Thanks to Bob’s double-Gaussian fit function; from proton data
σ=36μm
σ=54μm
σ=42μm
σ=41μm

## Slide 10: Residual distributions @ angles: REF3: 4mrad; UVA3: -17.35mrad; REF1: -48.5mrad
σ=27μm
σ=43μm
σ=44μm
σ=40μm

## Slide 11: Residual distributions @ angles: REF3: 4mrad; UVA3: -17.35mrad; REF1: -48.5mrad Exclusive fitting
σ=134μm
σ=77μm
σ=88μm
σ=91μm
11

## Slide 12: Residual distributions @ angles: REF3: 4mrad; UVA3: -17.35mrad; REF1: -48.5mrad Exclusive fitting
σ=99μm
σ=62μm
σ=73μm
σ=92μm
12

## Slide 13: Comparison of exclusive fitting and inclusive fiting (unit in μm in the table)
 | exclu. fittting | err | inclu. fitting | err | geo. Avg. | err
REF2X | 134 | 1.9 | 36 | 0.5 | 69.45502 | 1.378552
REF3X | 77 | 1.1 | 54 | 0.7 | 64.48256 | 1.243895
UVA3X | 88 | 1.1 | 42 | 0.9 | 60.79474 | 1.508192
REF1X | 91 | 1.5 | 41 | 0.7 | 61.08191 | 1.449585
REF2Y | 99 | 1.5 | 27 | 0.4 | 51.59651 | 1.095638
REF3Y | 62 | 1 | 43 | 0.7 | 51.63332 | 1.183241
UVA3Y | 73 | 1.1 | 44 | 0.7 | 56.67451 | 1.241881
REF1Y | 92 | 1.2 | 40 | 0.5 | 60.663 | 1.095941

## Slide 14: Some tracks
50 tracks @ same alignment/rotation parameters

## Slide 15: A thought on resolution study for radial (straight & zigzag) r/o detector—(r, phi)

## Slide 16: Summary
We now have better understanding on the tracking.
The fine alignment parameters for both mixed beam and proton beam data are figured out.
The rotation between detectors affects resolution on ref. detectors, but the affect can be corrected. The rotation angles can be calculated and tracking can be done by iterating these angles.
After we have these parameters, we can start working on resolution for probed detectors, need to work it out in (r, phi) plane…